## Slide 1: What physical factors affect runoff terms in the water balance?
Climate
Topography
Soils
Vegetation
Land-use

## Slide 2: Climate Factors
Precipitation
  Seasonal Cycle
  Intermittency
  Form (Rain or Snow)
Potential Evaporation
Temperature

## Slide 3: Topography
Slope
Aspect (Solar Radiation, Potential Evaporation)
Convergence
  Saturation and wetness index

## Slide 4: Topographic definition of contributing area, concentrated at a point or dispersed (specific catchment area) on a hillslope.

## Slide 5
Convergence Quantified Using Topographic Wetness Index
q = a r
S
qcap = T S
Saturation occurs when
Upslope area draining through a point within a catchment

## Slide 6
ln(a/S) wetness index for a small watershed evaluated from a 30 m Digital Elevation Model.

## Slide 7
Saturated area based on wetness index for two different T/r thresholds.

## Slide 8
Map of saturated areas showing expansion during a single rainstorm. The solid black shows the saturated area at the beginning of the rain; the lightly shaded area is saturated by the end of the storm and is the area over which the water table had risen to the ground surface. (from Dunne and Leopold, 1978)

## Slide 9: Soils
Infiltration capacity Ksat
Drainable porosity (saturated water content - water content at field capacity) x Depth
Field capacity (Water remaining after gravity drainage) x Depth
Erodability

## Slide 10
(a) Photograph of cross section through soil following dye tracing experiment. (b) Moisture content inferred from dye tracing experiment. (Courtesy of Markus Weiler)
Infiltration follows preferential pathways

## Slide 11: Vegetation
Density (leaf area index)
  Affects interception
Canopy conductance (relates ET to atmosphere vapor pressure deficit)
Root depth, strength and density (inhibit erosion and landslides)
Drives soil formation and responsible for preferential pathways

## Slide 12: Land use
Agriculture
  Irrigation withdrawals
  Erodibility
  Infiltration capacity
  Pollution (Manure, E. Coli, fertilizers, …)
Urbanization
  Impervious areas
  Water withdrawals
  Stormwater drains / soak pits
  Pollution
    Wastewater discharge
    Street runoff

## Slide 13
Horton overland flow dominates hydrograph; contributions from subsurface stormflow are less important
Direct precipitation and return flow dominate hydrograph; subsurface stormflow less important
Subsurface stormflow dominates hydrograph volumetrically; peaks produced by return flow and direct precipitation
Arid to sub-humid climate; thin vegetation or disturbed by humans
Humid climate; dense vegetation
Steep, straight hillslopes; deep,very permeable soils; narrow valley bottoms
Thin soils; gentle concave footslopes; wide valley bottoms; soils of high to low permeability
Climate, vegetation and land use
Topography and soils
Variable source concept
How do runoff processes depend on Climate, Vegetation, Land use, Topography and Soils?
(From Dunne and Leopold, 1978)

## Slide 14: Short time scale water balance
P
ET
Q
Gout
Gin
S
Retention fraction
Retention

## Slide 15: SCS Curve Numbers to Quantify Retention
CN=100
90
80
70
60
50
40
30
20

## Slide 17: Long Time Scale Water Balance
∆S=P-Q-E
P
E
Q
∆S
P=Q+E
Q=P-E

## Slide 18: P=Q+E
P
E
E=P
E=Ep
E
Q

## Slide 19: P=Q+E
P
E
E=P
E=Ep
E
Q
W=Q/P 0
W=Q/P 1

## Slide 20: Long Time Scale Water Balance and Runoff
Notes
P/Ep is an index of dryness
Reduced retention increases runoff
Imperviousness increases runoff
Variability in Q due to differences between large numbers, P-E
Greater relative sensitivity in arid areas
Q=P-E
Reducing Retention
Reducing Retention

## Slide 23
Generalised dependence
of Runoff Coefficient
and Style of Overland Flow on Arid-Humid scale and on Storm Rainfall Intensities
Seasonal or storm period fluctuations
(Slide courtesy of Mike Kirkby, University of Leeds, presented at AGU Chapman Conference on Hillslope Hydrology, 2001)

## Slide 24: What can we learn from considering seasonality in the long time scale water balance?
Low Retention
High Retention
Ep
P
P/Ep
Q/Ep
Ep
P
Low Retention
High Retention
Low Retention
High Retention
Q=f(P,Ep,S)

## Slide 25: Summer (in phase) seasonal precipitation
Low Retention
High Retention
Ep
P
P/Ep
Q/Ep
Ep
P
Low Retention
High Retention
Low Retention
High Retention
Q=f(P,Ep,S)

## Slide 26: Winter (off phase) seasonal precipitation
Low Retention
High Retention
Ep
P
P/Ep
Q/Ep
Ep
P
Low Retention
High Retention
Low Retention
High Retention
Q=f(P,Ep,S)

## Slide 27: Summary
Retention reduces runoff
Retention accentuates interaction with Ep
Arid climates (P < Ep) have greater relative sensitivity

## Slide 28: Other Considerations
Snow and snow storage
Spatial variability (elevation, temperature, orographic precipitation)
Quick flow versus base flow

## Slide 29: For a watershed you need to know
Upstream water management
  Reservoirs and diversions
Land-use and how it may change
Vegetation
Soils
Impervious areas
Saturated areas (topography)

## Slide 30: Geographic attributes you need to know
The watershed (area)
The stream network
Slope
Distance to stream

## Slide 31
100
10
1
0.1
0.001
0.1
10
1000
Area (sq. miles)
Walnut Gulch, AZ
Reisel, TX
Coshocton, OH
Reynolds Ck, ID
San Pedro, AZ
ID
AZ
TX
OK
OH
VA
GA
FL
MS
MO
PA
IA
Scale dependence of mean annual runoff for different geographic locations in the U.S. (Courtesy of David Goodrich, USDA-ARS).
Mean annual Runoff (inches)

## Slide 32
Flood wave advancing over a dry stream bed in Walnut Gulch experimental watershed where channel transmission losses are considerable. (Courtesy of David Goodrich, USDA-ARS)